## Slide 1: Managing Network Configurations with Git
Pete Lumbis - @PeteCCDE
Customer Solutions Engineer CCIE #28677, CCDE 2012::3

## Slide 2: $whoami
10+ year Network Engineer
2x top level Cisco Certified
Former Cisco senior support engineer
Design and builds datacenter networks
Not a programmer
Not a SysAdmin
Perl has 4 letters
So does Ruby
Python’s okay
My Background
Not My Background

## Slide 4: Git for Dummies
Source Code text file repository
Automatic file revision/change management
Built for teams to work on the same files
Easy to get started, lots of knobs for advanced users

## Slide 5: Git for Dummies - Glossary
Remote Repository – Central Server hosting files
Local Repository – Your local copy of the remote. Where you change things
Branch – Isolated copy for new features, risky changes
Merge – Apply branch changes to master repository copy (see also: “Pull Request”)

## Slide 6: Applying Git to Networking
Create changes in branches
master
IPv6
Merge and review
master
IPv6
Use merge/pull request as an opportunity to review impact of changes

## Slide 7: Applying Git to Networking (cont’d)
Rollback failures after merge
master
IPv6
Fork for new project/datacenter/office
east-dc
west-dc

## Slide 8: Using Git: The Good
Git is great at version control
Existing Tools Suck
  Rancid most common. SSH + diff
  $$$$ for pretty SSH + diff

## Slide 9: Using Git: The Bad
Implies “push” method
  Still need to get on-box changes committed back
No easy deployment
  Git manages code, not pushes files
One piece of a puzzle
  + Ansible, + Organization Behavior

## Slide 10: Using Git: The Ugly
Incumbent Vendors Bad at Rollback
Typos Cause Chaos
interface eth0
ip address 192.168.1.1 255.255.255.0
interface eth0
no ip address 192.168.1.1 255.255.255.0
interface eth0
no ip router isis
interface eth0
no router isis
Apply
Remove
Remove from single Interface
Remove all routing configuration

## Slide 11: In Action

## Slide 12: In Action!
Cumulus Linux
Cumulus Linux
Cumulus Linux
Cisco IOS
Leaf 1
Leaf 2
Spine 1
Spine 2

## Slide 13: Demo

## Slide 14: Takeaway
Git solves problems
  But not all of them
Network vendors need to provide better interfaces
  Separate state and configuration
New tools require new operational models
  NetOps, like DevOps, requires cultural shift

## Slide 16: Sidebar: Configuration vs State
A file containing what we want the system to do
/etc/network/interfaces
  auto eth0
  iface eth0 inet static
  address 192.168.1.1/24
What the system is doing right now.
ip addr add 192.168.1.1/24 dev eth0
cumulus@spine1$ ip addr show eth0 3: eth0: <BROADCAST,MULTICAST,UP,LOWER_UP> inet 192.168.1.1/24 scope global eth0
Configuration
State

## Slide 17: Anatomy of Network Configuration
Cisco/Juniper/Arista
  Running Configuration (current state)
  Startup Configuration (state loaded at boot)
  No state/config separation
Cumulus Linux (Linux based Switch OS)
  Debian standard state/configuration separation
  Configured exactly like a Linux server

## Slide 18: The Bad Old Days (Today)
When Configuration == State
  Log into production box
  Make changes, hope for best
  Copy state (running) into configuration (startup)
  Hope Rancid* works tonight to backup configuration
Notes: Rancid- http://www.shrubbery.net/rancid/